Sunsynk Inverter Class for pv_opt
using the solarsynk2 add-on for Home Assistant by martinville
Outstanding questions/issues or to be tested in red
Revision record (changes since last version in green):
Ver	Date	Details	By
1	17/2/2024	First version	MW
2	23/2/2024	Grid charge time x should be unticked for discharge according to Sunsynk. Inverter general description added, working modes clarified	MW
3	27/3/2024	MorneSaunders add-on. SellTime(x)Pac applies to discharge only. Charge current is limited by Grid Amps and Charge Amps. Work Mode must be changed in real time to enable battery discharge to grid	MW

# 1. General description of Sunsynk inverter
## 1.1 Input / output
Sunsynk inverters (e.g. ECCO 3.6kW hybrid inverter SYNK-3.6K-SG04LP1) have the following power inputs and outputs:
Direction	Name	Used for
Input	Solar PV	1 or 2 strings of Solar panels up to 350V DC
Output	Load	Uninterruptible Power Supply (UPS) / essential load i.e. power supply segregated from the grid which will continue to be supplied when the grid is down. Will normally be prioritised. Inverter has an optional ‘islanding mode signal’ which is on when the grid is down and an output which can be wired to a relay to disconnect inverter from grid and connect earth to neutral in the event of a grid outage (This reflects a strong history for the brand in southern Africa). When the grid becomes live again the inverter can detect it and automatically revert to grid mode after a delay. In simple domestic installations in the UK this output is not used because grid outages are uncommon and this requires segregated wiring in the house as well as some additional switches. This can cause confusion because ‘Load’ in Sunsynk terms refers to this UPS output only, not the normal house supply
Input/Output	Batteries	Numerous types and makes supported, including some types which are managed using voltage instead of State of Charge (SOC). In new UK domestic installations these would almost certainly be Lithium batteries with a battery management system and SOC support
Input/Output	Grid	Inverter is connected to the grid via a single circuit breaker on the consumer unit. Current can flow in either direction through this connection. Inverter distinguishes between Export and supply to non-essential loads in the house by using a CT clamp round the incoming live connection. Based on this it can supply just enough power to feed the domestic circuits if Export is disabled in the settings. To avoid transient currents flowing backwards through the meter (a problem in South Africa), it can maintain a configurable ‘Grid Trickle Feed’ flowing from the grid when it is also supplying the house from PV / battery. Export is also supported via the same connection
Input/Output	Auxiliary Load	This connection can be used either for input (Generator / Wind turbine) or output (a second segregated supply). If used for input, a box labelled ‘Gen’ can be ticked for each time slot in Timer mode to allow the batteries to be charged from this source. Peak shaving is supported (limit power take from Gen and supply the rest from the grid). If used for output, the software allows output to be turned on / off according to SOC settings

## 1.2 Inverter Parameters affecting import/export
Name	Options	What they do
Priority Load / {"energyMode": 0}	Priority Battery (1) / Priority Load (0)	Solar sent to batteries first / Solar sent to UPS Load first
Work Mode / {"sysWorkMode": 0}	Selling first (0) / Zero Export + Limit to Load only (1) / Limited to Home (2)	If timer is enabled and SOC > target SOC, battery will export until target SOC is reached / Battery used for UPS Load only (tbc) / Battery used for UPS and home but not export / [Solarsynk does not currently have a method of querying these settings so pv_opt can’t check them] / Work Mode cannot be set on a timer and must be changed to correct value in real time
Export Power Limiter / {"pvMaxLimit": 3600} (this appears to be correct but misleadingly named)	Normally set to the power of the inverter	If set lower, would reduce Export power from the figure against each Time slot / [Solarsynk does not currently have a method of querying these settings so pv_opt can’t check it. This could be a problem because pv_opt can set a power value against each time slow and we should check that it doesn’t exceed this figure]
Use Timer / {"peakAndVallery": "1"}	Tickbox (1)	If ticked, enables 6 individual time slots which have: / Start time / Whether batteries should be charged or discharged from Grid (tickbox) / Whether batteries should be charged from Gen (Auxiliary) input (tickbox) / Target SOC / Power limit
Charge Amps (Battery settings) / {"batteryMaxCurrentCharge": 50} tbc		Maximum charge current at battery voltage (presumably for all sources, not just Grid). Single setting for total of all batteries connected to inverter. Depends on rating of battery. On 2 x 5.12kWh batteries this was set to 90A by installer. This is well within the suppler recommended figure of 100A max per battery but reducing the figure increases battery life
Grid Charge / {"sdChargeOn": 1} tbc	Tickbox (1)	Whether batteries can be charged from grid
Grid Amps(0-275A) / {"sdBatteryCurrent": 50} tbc		Maximum charge current at battery voltage for charging from Grid. Should be no higher than Charge Amps (but may be adjusted to reach SOC slowly to increase battery life)
Discharge Amps (Battery settings) / {"batteryMaxCurrentDischarge": 50} tbc		Maximum discharge current at battery voltage On 2 x 5.12kWh batteries this was set to 90A by installer. This is well within the supplier recommended figure of 100A max per battery but reducing the figure increases battery life

### 1.3 Time of use mode
Sunsynk inverters have 6 timeslots. Each one has a settable start time; the end time of the previous slot adjusts to match. I think this means that slot 2 must start after slot 1 and slot 3 after slot 2 but I haven’t tested it. I think it is possible for one or more slots to contain 00:00 – 00:00 but I haven’t tested this. Obviously overlapping timeslots should be error trapped and also between them they should cover the whole 24 hour period. There is a ‘Use Timer’ mode tickbox. If this is not ticked I can’t see any way to force a charge or discharge
### 1.4 Live Price options
The Sunsynk app has a ‘Live Price’ mode which supports Octopus Flux and Octopus Agile. These are managed in the cloud so presumably work by setting Timer and SOC values on the inverter. I haven’t tried these yet but I believe the Flux option would use the timers to charge to 100% in the cheap window, discharge to 20% in the Peak, and maintain a minimum 20% the rest of the time (a total of at least 4 slots). The Agile option seems to be a work in progress, there have been some problems with it. User can set min price for exporting from battery and max price for charging. I’ve heard that this works by updating the first 2 slots every 30mins (and presumably leaving the other 4 set to 00:00 – 00:00 but I haven’t tested this). As far as I can see it doesn’t take forecast PV into account so is less efficient than pv_opt

# 2. Sunsynk Integrations / Add-ons for Home Assistant
I know of 3 Sunsynk integrations for Home Assistant:
## 2.2 Deye/Sunsynk Home Assistant add-on by kellerza in GitHub
This requires a direct connection to the inverter via RS485
I didn’t use this one because it requires direct wiring and in some more modern Sunsynk inverters needs to share a single port on the inverter with a cable to the battery
## 2.3 Solar-Sunsynk Home Assistant Add-on by MorneSaunders in GitHub
I haven’t tried this and don’t know much about it but it uses the Sunsynk.net cloud API and has a Home Assistant Service which can be called to adjust inverter settings

## 2.4 Solarsynk2 add-on by martinville in GitHub
### 2.4.1 Connection method
Connects to the inverter via the Sunsynk.net cloud API used by the Sunsynk app. (nb Sunsynk have recently completed a migration from a Solarman integration which used a Solarman WiFi dongle. They refer to this as ‘Region 1’. Solarsynk2 only works with the Sunsynk API, known as ‘Region 2’). Data in the cloud is updated every 5 mins by a Sunsynk branded WiFi datalogger directly connected to the inverter. Consequently, the add-on is also set by default to poll the cloud every 5 mins
### 2.4.2 Updates
Updates to inverter settings are sent to the cloud by the same 5 min batch process. The add-on checks to see if any settings have been populated in a Helper called input_text.solarsynk_{inverter_sn}_settings. {inverter_sn} is defined manually in the pv_opt config. Data is in json format e.g:

{"sellTime2": "02:30","sellTime2Pac": "3599"}

If so, it posts them to the cloud, outputs the response to the log, and empties the Helper. Output is like this (inverter serial number redacted):

Updating Helper: input_text.solarsynk_xxxxxxxxxx_inverter_settings with: {"sellTime2": "02:30","sellTime2Pac": "3599"} / { / "code": 0, / "msg": "Success", / "data": null, / "success": true / } / Clearing previously set temporary settings.

It is possible to update multiple settings at the same time but by default the Helper is limited to 100 text chars. Response seems to be immediate but I don't know if that means the inverter has definitely been updated or is just a response from the cloud. The inverter seems to be updated straight away – at least before I can get into the loft to see the results. Log is the standard HA log visible from within the Solarsynk add-on

It may be that we need the update to be quicker than waiting up to 5 mins for pv_opt and for the response to be more accessible. I’ve asked martinville if he would add a real time method of update. He says he is limited by the technology of the add-on (a Bash script) and doesn’t want to make major alterations to the project but will give it some thought
### 2.4.3 Required Class attributes
NB in the notes below the settings for each of the timed slots are denoted by setting(x) where (x) is 1-6. The brackets should be ignored e.g
sellTime(x) = sellTime1, sellTime2, sellTime3, sellTime4, sellTime5, sellTime6
time(x)on = time1on, time2on, time3on, time4on, time5on, time6on
and so on

pv_opt attribute	Solarsynk entity	Sunsynk json key	Comments
maximum_dod_percent	sensor.solarsynk_{inverter_sn}_battery_shutdown_cap	Battery Shutdown cap:{"batteryShutdownCap": 15} / or Low Batt: {"batteryLowCap": 20}	Shutdown %
update_cycle_seconds	Refresh_rate: 300		In add-on yaml
supports_hold_soc			There isn’t a ‘mode’ for this – one target SOC is set for each timer – means minimum when discharging, maximum when charging
Battery minimum state of charge	sensor.solarsynk_{inverter_sn}_battery_shutdown_cap	Battery Shutdown cap:{"batteryShutdownCap": 15} / or Low Batt: {"batteryLowCap": 20}
id_battery_soc	sensor.solarsynk_{inverter_sn}_battery_soc		Current SOC
id_consumption_today	sensor.solarsynk_{inverter_sn}_day_load_energy		kWh since midnight
id_grid_import_today	sensor.solarsynk_{inverter_sn}_day_grid_import		kWh imported from grid since midnight
id_grid_export_today	sensor.solarsynk_{inverter_sn}_day_grid_export		kWh exported to grid since midnight
battery_voltage	sensor.solarsynk_{inverter_sn}_battery_voltage		Current battery voltage
id_timed_charge_start_hours	sensor.solarsynk_{inverter_sn}_prog(x)_time	"sellTime(x)": "16:00"	6 slots, (x) = 1-6. Contains both hours and minutes in the form hh:mm
id_timed_charge_start_minutes			See above
id_timed_charge_end_hours		"sellTime(x+1)": "19:00"	No separate setting – it is defined by the start time of the next slot i.e. x+1
id_timed_charge_end_minutes			See above
id_timed_charge_current	[can’t find an HA sensor for this]	{"sdBatteryCurrent": 50}	Should be no greater than Battery charge amps {"batteryMaxCurrentCharge": 50} / For Sunsynk L5.1 (5kWh) batteries recommended value is no more than 50A @ 50V
charge	Set / Start time for relevant slot (x) sensor.solarsynk_{inverter_sn}_prog(x)_time / Start time for next slot / sensor.solarsynk_{inverter_sn}_prog(x+1)_time / Tick Grid charge time (x) / sensor.solarsynk_{inverter_sn}_prog(x)_charge / Set target SOC for this slot sensor.solarsynk_{inverter_sn}_prog(x)_capacity / Set Max Grid Amps for charging	"sellTime(x)": "02:00" / "sellTime(x+1)": "05:00" / "time(x)on": true / "cap(x)": "80" / {"sdBatteryCurrent": 50}	Battery will charge from Grid during this time slot if current SOC is lower than target SOC(x) e.g. "cap(x)": "100" / Setting a time automatically sets end time for previous slot / Labelled ‘Grid’ with a tickbox next to each timer on inverter and ‘Grid Charge Time(x)’ in app / [sellTime(x)Pac apples to discharge only, not charge]
Discharge	Set : / Start time for relevant slot (x) sensor.solarsynk_{inverter_sn}_prog(x)_time / Start time for next slot (automatically sets end time for this slot) / sensor.solarsynk_{inverter_sn}_prog(x+1)_time / Untick Grid for relevant slot (x) / sensor.solarsynk_{inverter_sn}_prog(x)_charge / Target SOC for this slot sensor.solarsynk_{inverter_sn}_prog(x)_capacity / Set Power for this slot / sensor.solarsynk_{inverter_sn}_battery_shutdown_cap	"sellTime(x)": "16:00" / "sellTime(x+1)": "19:00" / "time(x)on": false Labelled ‘Grid’ with a tickbox next to each timer on inverter and ‘Grid Charge Time(x)’ in app / "cap(x)": "20" / "sellTime(x)Pac": "3600" / "batteryShutdownCap": "15"	Same timeslots as above but Grid is unticked and Target SOC is lower. Battery will discharge to grid during this time slot if current SOC is higher than target SOC(x) e.g "cap(x)": "20" / Work Mode is normally set to 2 = Limited to Home. If batteries are to be discharged for Export, Work Mode must be set to 0 = Selling First at start of slot, and set back to 2 = Limited to Home at the end in real time / [Should be no higher than Export Power Limiter but there is currently no method in Solarsynk to query this] / Also should check that target SOC is not lower than battery shutdown capacity
hold_soc			There is no mode for this – use timers instead

### 2.4.4 Required Class methods
NB the usual manual way to set a timed charge for a Sunsynk inverter / battery system is to set Grid Charge Amps to an appropriate level for the timed slot and use a target SOC to turn off when the desired state is reached. For discharging the usual manual method is to set power to an appropriate level for the timed slot and use a low target SOC to turn off when complete (say 20% which is the default shutdown SOC for the battery).
Work Mode is normally set to Limited to Home =2 which prevents export from battery but still allows export of excess Solar. To deliberately discharge the battery to the Grid, Work Mode should be set to Selling First = 0 in real time at the start of the timed slot and back to Limited to Home = 2 at the end This can only be done in real time, there is no option for this in the timer
Which timeslots to use? The timeslots need to avoid overlap, be in the right order, and cover 24 hours so all 6 should be set at the same time. Not all slots have to be used – they can be set 00:00 – 00:00
For Octopus Flux we need 5:
- 1. 00:00 – start charge
- 2. start charge – end charge
- 3. end charge to start discharge
- 4. start discharge – end discharge
- 5. end discharge – 00:00
- 6. not required so should be 00:00
For Octopus Agile we could use:
- 1. 00:00 – this 30min
- 2. this 30min – next 30min
- 3. 30min slot 2
- 4. 30min slot 3
- 5. 30min slot 4
- 6. end 30min slot 4 – 00:00

Normally we want battery to be available to power the home if Solar is insufficient so unless deliberately charging fro the Grid, timed slots should be set to discharge. To avoid exporting to the Grid, Work Mode must be set to Limited to Home = 2. To export from Battery to the Grid, Work Mode must be changed to Selling First = 0 at the start of the timed slot and back to Limited to Home = 2 at the end

pv_opt method	Parameter / relevant Solarsynk entities	Sunsynk fields to update	Steps
.enable_timed_mode()	sensor.solarsynk_{inverter_sn}_use_timer / sensor.solarsynk_{inverter_sn}_battery_type / sensor.solarsynk_{inverter_sn}_overall_state / sensor.solarsynk_{inverter_sn}_grid_connected_status / [Can’t see an HA sensor for this]	{"peakAndVallery": "1"} / [nb this is not a misspelling of peakAndValley] / {"battMode": "-1"} tbc	Tick ‘Use Timer’ if not already ticked / In addition, check that: / 1. Battery type is Lithium. This ensures battery supports SOC sensor.solarsynk_{inverter_sn}_battery_type = 1. / 2. Inverter state is Normal / 3. Grid connection status = 1 / 4. Ideally we would check that the Auxiliary input/output is not connected but Solarsynk doesn’t currently have a method for this so the best we can do is disable charge from Gen in the timers
.control_charge()	Enable / Start / End (optional) / Grid Amps for charging / Gen charge x	"cap(x)": "100" / "time(x)on": true / "sellTime(x)": "02:00" / "sellTime(x+1)": "05:00" / {"sdBatteryCurrent": 50} / "genTime(x)on": false	Target SOC for this timeslot needs to be set to a high value e.g. 100% / Set Grid charge time(x) = true / Probably need to clear times from all other timers to avoid overlap / Set Start Time. I think this needs to be mandatory for sunsynk, I can’t see any other way to force a charge / Set Start Time for timer x+1. If missing, assume 00:00. If x is 6 (i.e. last slot, set Start Time for timer 1 / Must be no higher than battery recommended figure ("battery MaxCurrentCharge") (50A recommended for Sunsynk L5.1) / "sellTime(x)Pac": "3600" applies to discharge only / If ticked, will allow charging from Gen (Auxiliary) input. [I imagine this would invalidate the pv_opt calculations so should be set to 0 in all timeslots] [Solarsynk doesn’t currently have a method of determining whether the Auxiliary is connected]
.control_discharge()	Enable / Start / End (optional) / Power / Gen charge x	"cap(x)": "20" / "time(x)on": true / "sellTime(x)": "02:00" / "sellTime(x+1)": "05:00" / "sellTime(x)Pac": "3600" / "genTime(x)on": false	Target SOC for this timeslot needs to be set to a low value e.g. 20%. / Probably need to clear times from all existing timers to avoid overlap / Set Grid charge time(x) = true / Set Start Time. I think this needs to be mandatory for Sunsynk, I can’t see any other way to force a charge / Set Start Time for timer x+1. If missing, assume 00:00. If x is 6 (i.e. last slot, set time for timer 1 / Set Power(x) to limit charge power during the time slot x. Must be no higher the inverter / battery rating / If ticked, will allow charging from Gen (Auxiliary) input. [I imagine this would invalidate the pv_opt calculations so should be set to 0 in all timeslots] [Solarsynk doesn’t currently have a method of determining whether the Auxiliary is connected]
.hold_soc()			There isn’t a mode for this, just use timers